Mantis Minerals Corp. has commenced exploration on its Orphan Gold Mine property

Toronto, Ontario – July 3,2007- Mantis Mineral Corp (‘Mantis’--CNQ ‘MINT’) is pleased to announce results of its initial field examination of its 100% owned Orphan Gold Mine property located in the Thunder Bay Mining Division west of Geraldton, Ontario.

This examination has confirmed the continuity of the “main vein” from which historical sample sites grading 11.52 ounces per ton gold (394.97 grams per tonne) and 1.816 ounce per ton gold (62.26 grams per tonne) have been reported from samples of trenches along the “main vein”.

A parallel vein system has also been discovered, designated the “north vein” and is situated 100-meters northeast of the main vein. It has been intermittently traced by previous trenches along a 41-meter length and remains open on strike at both ends.

The “main vein” along which underground and surface work was concentrated historically has been geo-referenced to the underground workings and existing surface trenches. This vein trends at azimuth 140 to 160-degrees, and has been traced northwest of the shaft for 76-meters. The length of the vein traced on surface on the property is estimated at 136-meters. The system remains open at both ends.

All relevant surface workings, underground workings and structures are in the process of being compiled to the GIS database to develop a 3D model of the vein. This model will be used extensively to design a drill program to test the multiple vein systems.

Mantis will commence shortly a program of mechanical stripping and trenching on its own findings and the recommendations of Caracle Creek International Consulting Ltd., an independent evaluator who has prepared a National Instrument 43-101 on the property. This program will further expose the extent of the “main and north” vein(s) and alteration halos for the purpose of channel sampling and mapping. This program will also be examining other surface showings confirmed by the initial field examination. The data gathered from this program will be incorporated into the model to assist with design and implementation of a follow-up drill program.

“This is an exciting time for the exploration of this property as it is  located in an historically rich gold belt.  We are looking forward to advancing the development of this previously producing gold mine, “ commented Robin Ross, CEO.

Mantis Mineral Corp. is a Canadian exploration company with a portfolio of quality gold and base metal properties located in mining friendly northern Ontario.

The CNQ Exchange has not reviewed and does not accept responsibility for the adequacy of this release.

FOR FURTHER INFORMATION PLEASE CONTACT:

Mr. Robin Ross, Chairman & CEO 		 (416) 362-1800

rross@mantismineralcorp.com

NEWS RELEASE TRANSMITTED BY CNW Group